## Slide 1
Image Processing is a method to convert an image into digital form and perform some operations on it, in order to get an enhanced image or to extract some useful information from it.
Usually Image Processing system includes treating images as two dimensional signals while applying already set signal processing methods to them.
Image Processing(CO1)

## Slide 2
An image defined in the real world is considered to be a function of two real variable say x, y .
Before going to process an image, it is converted into a digital form. Digitization includes sampling of image and quantization of sampled values.
After converting the image into bit formation, Processing is performed.
This processing technique may be,
Image enhancement
Image reconstruction
Image compression
Image Processing

## Slide 3
Image Processing
Image enhancement refers to accentuation , or sharpening of image features such as boundaries.
Image restoration is concerned with filtering the observed image to minimize the effect of degradations.
Image compression is concerned with minimizing the number of bits required to represent an image.
Text compression – CCITT Group3 and Group4
Still image compression – JPEG
Video image compression- MPEG

## Slide 4
Image Processing basically includes following three steps:
Importing the image with optical scanner or by digital photography.
Analyzing and manipulating the image which includes data compression and image enhancement and spotting patterns that are not to human eyes like satellite photographs.
Output is the last stage in which result can be altered image or report that is based on image analysis
Image Processing Steps
4

## Slide 5
Types of Image Processing
5
There are two types of image processing :
Analog image processing
It refers to the alteration of image through electrical means.
Most common example is television image.
2. Digital Image Processing
In this case , digital computers are used to process the image.
Image will be converted into a digital form using a scanner – digitizer and then it will process it.

## Slide 6
Computer Vision
Face detection
Microscope image processing
Agricultural application
Remote sensing
Medical imaging
Forensic studies
Graphics arts
Applications
6

## Slide 7
An image file format is a specific way in which image data is encoded and stored in a file. Different image file formats have different characteristics, such as the method of compression, color representation, support for transparency, and metadata storage.
Image File Format (CO1)

## Slide 8
Here are some commonly used image file formats
JPEG/JPG (Joint Photographic Experts Group): JPEG is a widely used compressed image format that supports millions of colors. It is commonly used for photographs and complex images. JPEG files can achieve high compression ratios, but they are lossy, meaning that some image quality may be sacrificed to reduce file size.
PNG (Portable Network Graphics): PNG is a lossless image format that supports transparency. It is often used for web graphics, icons, and images that require high-quality and lossless compression. PNG files support both RGB and grayscale color spaces.
Commonly used image File Format

## Slide 9
Continued…
GIF (Graphics Interchange Format): GIF is a compressed image format that supports animation and transparency. It uses a limited color palette (up to 256 colors) and is commonly used for simple graphics, logos, and animations.
BMP (Bitmap): BMP is a basic raster image format that stores individual pixels as color values. It does not use compression, resulting in larger file sizes compared to other formats. BMP files can store images with various color depths and are commonly used in Windows environments.

## Slide 10
Continued…
TIFF (Tagged Image File Format): TIFF is a flexible image format that supports lossless compression and can store multiple images in a single file. It is commonly used in professional printing and publishing and can maintain high image quality.
RAW: RAW is not a specific file format but rather a term used to describe unprocessed image data captured by digital cameras. RAW files contain the raw sensor data without any compression or processing, allowing for greater flexibility in post-processing.

## Slide 11
Geometric Modeling is the computer/software-generated mathematical representation of an object’s geometry. It includes both graphical and non-graphical information. This information is stored in a database and displayed as a picture. It is then possible to edit and analyze the model in different ways.
The mathematical representation of an object can be displayed on a computer and used for the generation of drawings, which go on for analysis and eventual manufacturing of the object.
Geometric Model (CO1)

## Slide 12
In general, there are three conventional steps to creating a geometric model:
They create key geometric elements using commands like points, lines, and circles.
Applying Transformations on the geometric elements using commands like rotation, achieve scaling, and other related transformations functions.
Construct the geometric model using various commands that integrate the geometric model's elements to form the desired shape.
Continued…
12

## Slide 13
Representation of Geometric model
There are two basic types of geometric models: a two-dimensional model, which is used for technical drawing, and a three-dimensional model, which is used for computer-aided design and manufacturing.
Two-Dimensional or 2D: It projects a two-dimensional view and is used for flat objects.
Three-Dimensional or 3D: This representation permits complete three-dimensional viewing of the model with intricate geometry. The leading process of geometric modeling in 3D is Solid modeling.

## Slide 14
14
Types of Geometric Modeling
Depending upon the representations of objects, geometric modeling system can be classified into three categories, which are:
Wireframe modelling
Surface modelling
Solid modeling

## Slide 15
It is a simple modeling system used to represent the object with the help of lines only. Hence, it is also known as Line model representation. However, wireframe modeling is not enough to express complex solids; therefore, it is used to describe only wiring systems.
Wireframe geometric modeling is a good option for small-scale companies, where intricate surface details are essential for product design.
Wireframe Modeling

## Slide 16
Continued…
16

## Slide 17
Can quickly and efficiently convey information than
multiview drawings.
Can be used for finite element analysis.
Can be used as input for CNC machines to generate
simple parts.
Contain most of the information needed to create surface, solid and higher order models
Wireframe Modeling – Advantages

## Slide 18
Wireframe Modeling – Disadvantages
Tend to be not realistic
Do not represent an actual solids (no surface and volume).
Cannot model complex curved surfaces.
Cannot be used to calculate dynamic properties.

## Slide 19
Surface Modeling
Surface Modeling is another popular method. This type of modeling represents the object by its surface and is used to describe the object with a clear view of manufacturing.
This method uses surface geometry to create objects with complex forms. From this clear point of view, surface modeling cannot be used to develop an internal surface of any model. Surface modeling uses Bezier and B-spines.
Surface modeling is better for design engineers as it organizes the edges that define polygonal surfaces.

## Slide 20
Surface Modeling – Advantages and Disadvantages
Advantages:
Eliminates ambiguity and non-uniqueness present in wireframe models by hiding lines not seen.
Provides the surface geometry for CNC machining.
Provides the geometry needed for mold and die design.
Can be used to design and analyze complex free-formed surfaces (car bodies)
Disadvantages:
Surface models provide no information about the inside of an object.
Cannot be used to calculate dynamic properties.

## Slide 21
Solid Modeling
Solid modeling also known as volume modeling, this is the most widely used method, providing a complete description of solid modeling. Solid modeling tools allow you to build many sides of an object at once. Solid models make multiple sides at once, reducing the ambiguity in surface modeling.

## Slide 22
Solid Modeling – Advantages and Disadvantages
Advantages:
Has all the advantages of surface modelling plus volumetric information.
Allows the designer to create multiple options for a design.
2D standard drawings , assembly drawing and exploded views are generated form the 3D model.
Can easily be exported to different finite element methods program for analysis.
Disadvantages:
More intensive computation than wireframe and surface modelling.
Requires more powerful computers

## Slide 23
Photometric Model (CO1)
In image processing, a photometric model refers to a mathematical model that describes the relationship between the physical properties of light and the resulting pixel values in digital images. It helps to understand and manipulate the photometric characteristics of images, including brightness, contrast, and color.
Photometric models are used to simulate and understand the process of capturing light by imaging sensors such as cameras. They take into account factors such as the illumination conditions, reflectance properties of objects, and sensor characteristics to predict the pixel values in an image.

## Slide 24
Continued…
Commonly used photometric models include:
Lambertian Reflectance Model: This model assumes that the light reflected from an object's surface is diffusely scattered in all directions. It is often used for matte surfaces that exhibit uniform reflectance properties.
Phong Reflectance Model: This model extends the Lambertian model by considering the specular reflection component. It takes into account the angle between the viewer's line of sight and the surface normal to simulate the glossy reflection of light.

## Slide 25
Continued…
Bidirectional Reflectance Distribution Function (BRDF): BRDF is a more complex photometric model that accounts for the reflectance properties of surfaces at different angles of incidence and observation. It provides a detailed description of how light is scattered and reflected from surfaces

## Slide 26
Image digitization (CO1)
Image digitization captured by a sensor is expressed as a continuous function f(x,y) of two co-ordinates in the plane.
Image digitization means that the function f(x,y) is sampled into a matrix with M rows and N columns.
The image quantitation assigns to each continuous sample an integer value.
The continuous range of the image function f(x,y) I split into K intervals.

## Slide 27
Image digitization
The finer the sampling (i.e., the larger M and N) and quantitation (the larger K) the better the approximation of the continuous image function f(x,y).
Two questions should be answered in connection with image function sampling:
  First, the sampling period should be determined the distance between two neighboring sampling points in the image.
  Second, the geometric arrangement of sampling points (sampling grid) should be set.

## Slide 28
Sampling and Quantization(CO1)
The output of most of the image sensors is an analog signal, and we can not apply digital processing on it because we can not store it. We can not store it because it requires infinite memory to store a signal that can have infinite values.
So we have to convert an analog signal into a digital signal.
To create an image which is digital, we need to covert continuous data into digital form. There are two steps in which it is done.
Sampling
Quantization

## Slide 29
Continued…
We will discuss sampling now, and quantization will be discussed later on but for now on we will discuss just a little about the difference between these two and the need of these two steps.
Basic idea:
The basic idea behind converting an analog signal to its digital signal is to convert both of its axis (x,y) into a digital format.

## Slide 30
Continued…
Since an image is continuous not just in its co-ordinates (x axis), but also in its amplitude (y axis), so the part that deals with the digitizing of co-ordinates is known as sampling. And the part that deals with digitizing the amplitude is known as quantization.

## Slide 31
Concept of Sampling
Sampling is done only on an independent variable. For example, if we digitize x-axis in sampling.
y=sinx (it is done on variable x)
Sampling is divided into two parts:
1. upsampling
2.downsampling
There are variations in the sampled signal which is due to noise. To reduce the noise more samples are taken which means more data or pixel which result in a better image with less noise present in it.

## Slide 32
Continued…

## Slide 33
What is Quantization?
Quantization is a lossy compression technique which is achieved by compressing a range of values to single quantum. In other words, we can also say that it is a process of converting a continuous range of values into a finite range of discrete values. In a given stream when discrete symbols are reduced then, the stream becomes more compressible.
For example, when we reduce the number of colors in a digital image the file size is also reduced.
Applications such as DCT data quantization in JPEG and DWT data quantization in JPEG 2000 are used.

## Slide 34
Continued…
As we know that bits are used to represent a pixel intensity, which is limited that is why quantization is needed.
If 8 bit is used for a pixel which is in the range from 0 to 255 where 0 is used for pure black and 255 is used for pure white and the intermediate values are used for gray color.
level 257, and the quantized image is of quantization level 16. In the above images, the original image is of quantization

## Slide 35
Image Definition(CO1)
It is an array of matrix pixel(picture elements) arranged in columns and rows.
An image is also two-dimensional array specifically arranged in rows and columns. Digital image is composed of picture elements image elements and pixels.
A pixel is most widely used to denote the elements of the digital image.

## Slide 36
Image Representation
﻿
After an image is segmented into regions; the resulting aggregate of segmented pixels is represented & described for further computer processing.
Representing a region involves two choices:
  in terms of its external characteristics (boundary)
  in terms of its internal characteristics (pixels comprising the region)
Above scheme is only part of task of making data useful to computer.
Next task is to Describe the region based on representation.
Ex. A region may be represented by its boundary & its boundary is described by features such as its length, the orientation of straight line joining its extreme points & number of concavities in the boundary.

## Slide 37
Image Representation
﻿
Q. Which to choose when?
External representation is chosen when primary focus is on shape characteristics.
Internal representation is chosen when primary focus is on regional properties such as color & texture.
Sometimes it is necessary to choose both representations.

## Slide 38
Image Representation
﻿
It deals with compaction of segmented data into representations that facilitate the computation of descriptors.
1) Boundary (Border) Following:
Most of the algorithms require that points in the boundary of a region be ordered in a clockwise (or counterclockwise)
direction.
We assume
  i) we work with binary images with object and background represented as 1 & 0 respectively.
  ii) Images are padded with borders of 0s to eliminate the possibility of object merging with image border.

## Slide 39
Image Representation

## Slide 40
Image Representation

## Slide 41
Image Representation

## Slide 42
Image Representation
﻿
5) Repeat step 3 & 4 until b = b0 & next boundary point found is b1. The sequence of b points found when the algorithm stops constitutes the set of ordered boundary points.
The algorithm is also called as Moore boundary Tracking algorithm.

## Slide 43
Image Representation

## Slide 44
Image Representation
﻿
A boundary code formed as a sequence of such directional numbers is referred to as a Freeman chain code.
Digital images are acquired & processed in a grid format with equal spacing in x and y directions.
So a chain code can be generated by following a boundary (say clockwise direction) and assigning a direction to the segments connecting every pair of pixels.
Unacceptable method: (because)
  1) Resulting chain tends to be quite long
  2) Any small disturbances along the boundary due to noise or imperfect segmentation can cause changes in code.

## Slide 45
Image Representation

## Slide 46
Image Representation
A solution to this problem is to resample the boundary by selecting a larger grid spacing.
Then, as the boundary is traversed, a boundary point is assigned to each node of the large grid, depending upon the proximity of original boundary to that node.
The re-sampled boundary can now be represented by a 4- or 8-code.
The accuracy of the resulting code representation depends on the spacing of the sampling grid.

## Slide 47
Image Representation
﻿
3) Polygon Approximation using Min. Perimeter Polygons:
A digital boundary can be approximated with arbitrary accuracy by a polygon.
For a closed boundary, approx becomes exact when no. of segments of polygon = no. of points in the boundary.
Goal of poly. Approx is to capture the essence of the shape in a given boundary using fewest no. of segments.
Min. Perimeter Polygon (MPP):
An approach for generating an algorithm to compute MPPs is to enclose a boundary by a set of concatenated cells.
Think boundary as a rubber band.
As allowed to shrink, it will be constrained by the inner & outer walls of the bounding regions.

## Slide 48
Image Representation

## Slide 49
Image Representation
This shrinking produces the shape of a polygon of min. perimeter.
Size of cells determine the accuracy of the polygonal approximation.
In the limit if size of each cell corresponds to a pixel in the boundary, the error in each cell between the boundary & the MPP approx. at most would be v2d, where d-min possible pixel distance.

## Slide 50
Image Representation
The objective is to use the largest possible cell size acceptable in a given application.
Thus, producing MPPS with fewest no. of vertices.
The cellular approach reduces the shape of the object enclosed by the original boundary to the area circumscribed by the gray wall.
Fig. shows shape in dark gray.
Its boundary consists of 4-connected straight line segments.

## Slide 51
Image Representation
If we traverse the boundary in counter clockwise direction.
Every turn encountered in the transversal will be either a convex (white) or concave (black) vertex, with the angle of vertex being an interior angle of the 4-connected boundary.
Every concave vertex has a corresponding mirror vertex in light gray wall, located diagonally opposite.
MPP vertices coincide with the convex vertices of inner wall and mirror concave vertices of outer wall.

## Slide 52
Image Representation

## Slide 53
Neighbourhood Metrics(CO1)
In image processing, neighboring matrices, also known as neighborhood matrices or convolutional kernels, are small square or rectangular matrices used to process and analyze pixels in an image. These matrices are applied to each pixel in the image to perform various operations such as filtering, smoothing, edge detection, and feature extraction.
Neighboring matrices are typically of odd dimensions (e.g., 3x3, 5x5, 7x7) to ensure a center pixel. The values within the matrix, often referred to as weights or coefficients, determine the specific operation performed on the pixel and its neighboring pixels.

## Slide 54
Neighbourhood Metrics
One common operation using neighboring matrices is convolution. Convolution involves taking the element-wise product of the neighboring matrix with the corresponding pixel values in the image, summing up the results, and placing the result at the center pixel. This process is repeated for every pixel in the image, effectively applying the same operation to each pixel.

## Slide 55
Neighbourhood Metrics
Neighboring matrices can also be used for other operations such as edge detection. For instance, the Sobel operator uses two 3x3 neighboring matrices to detect vertical and horizontal edges in an image by computing gradients. These matrices have different weight distributions that emphasize changes in pixel intensity along the horizontal and vertical directions.
Overall, neighboring matrices play a crucial role in image processing as they allow for localized analysis and manipulation of pixel values, enabling various image enhancement and feature extraction techniques.

## Slide 56
Faculty Video Links, Youtube & NPTEL Video Links and Online Courses Details
https://www.youtube.com/watch?v=Y_-HgmvF9Zc
https://www.youtube.com/watch?v=MiSS_aEEf8w
https://www.youtube.com/watch?v=F3ZvWQMyj4I
https://www.youtube.com/watch?v=onWJQY5oFhs
https://www.youtube.com/watch?v=ecu8kreTwYM
https://www.youtube.com/watch?v=7ImSbCj8bRI
https://www.youtube.com/watch?v=yKFaHFwTg00

## Slide 57
1) What is the first and foremost step in Image Processing?
Image Restoration
Image Enhancement
Image Acquisition
Segmentation
2) _____ is called matrix of each element…
a) pixels
b) value
c) coordinate
d) dots
MCQ

## Slide 58
3. Which of the following process helps in Image enhancement?
a) Digital Image Processing
b) Analog Image Processing
c) Both a and b
d) None of the above
4. Which of the following is an example of Digital Image Processing?
a) Computer Graphics
b) Pixels
c) Camera Mechanism
d) All of the mentioned
MCQ

## Slide 59
5. What are the categories of digital image processing?
a) Image Enhancement
b) Image Classification and Analysis
c) Image Transformation
d) All of the mentioned
6. Which of the following is the first and foremost step in Image Processing?
a) Image acquisition
b) Segmentation
c) Image enhancement
d) Image restoration
MCQ

## Slide 60
7. Which of the following image processing approaches is the fastest, most accurate, and flexible?
a) Photographic
b) Electronic
c) Digital
d) Optical
8. Image processing involves how many steps?
a) 7
b) 8
c) 13
d) 10
MCQ

## Slide 61
Explain about HSI color model?
Discuss all the components of an image processing system.
Define an image. List out and explain the various areas of applications of image processing.
Explain about RGB color model in detail.
Old Question Papers

## Slide 62
1. What do you mean by image processing system. Mention some of its Application.
2. Explain basic image file format.
3. Explain Geometric modeling and its type in detail.
4. What do you mean by image digitization.
5. Explain image representation in detail.
Assignment

## Slide 63
Thank You